## Slide 1: Smart Monitoring And Safety System Phase 1

## Slide 4
Device | Pin on Device | Raspberry Pi 5 Pin | Notes
TMP117 #1 | VIN | 3.3 V (Pin 1) | 
 | GND | GND (Pin 9) | 
 | SCL | GPIO 3 (Pin 5) | 
 | SDA | GPIO 2 (Pin 3) | 
 | ADDR | 3.3 V (Pin 1) | I2C Address 0x49
 | INT | GPIO 17 (Pin 11) | 
TMP117 #2 | VIN | 3.3 V (Pin17) | 
 | GND | GND (Pin25) | 
 | SCL | GPIO 3 (Pin 5) | 
 | SDA | GPIO 2 (Pin 3) | 
 | ADDR | GND (Pin 9) | I2C Address 0x48
 | INT | GPIO 27 (Pin 13) | 
HC-SR501 | VCC | 5V (Pin 2) | 
 | GND | GND (Pin 6) | 
 | OUT | GPIO 23 (Pin 16) | 
I2C Pull-ups: 4.7kΩ on SDA & SCL to 3.3V |  |  | 
Interrupt Pull-ups: 10kΩ to 3.3V on each INT pin |  |  | 
100nF (0.1µF) capacitor between VIN and GND of each TMP117 sensor (mandatory) |  |  | 
1µF (optional) if long wires are used |  |  | 
Component | Connection
Buzzer +ve (VCC) (long leg) | 5V (Pin 2)
Buzzer -ve (GND) (short leg) | Collector of transistor
Emitter of transistor | GND (Pin 34)
Base of transistor | Through 1kΩ resistor to GPIO 25 (Pin 22)
Diode (1N4007/1N4148) | Parallel with buzzer (Cathode to 5V, Anode to transistor collector)
Transistor (e.g., 2N2222, BC547) acts as a switch | 
1kΩ Resistor limits the current to the transistor’s base | 
Buzzer turns ON when GPIO 25 is set HIGH | 
GPIO Devices wiring diagram

## Slide 5: Smart Monitoring And Safety System Phase 2 - Addition of HC-SR501 PIR motion sensor